Q1.
The ethernet address of my computer is
08:ed:b9:a1:76:95

Q2.
The destination ethernet address is
00:00:0c:9f:f0:00.

No, it is the address of the router which takes me out of our own subnet.

Q3.
The frame type field is 0X0800.
It corresponds to the protocol to which the payload of this frame will be given i.e, IP. It can be seen in the screenshot.

Q4.
As seen in the hexadecimal dump in the screenshot, it appears after 66 bytes.

Q5.
The ethernet source address is 00:00:0c:9f:f0:00. It is the address of the router that takes us out of our network.

Q6.
The destination address 00:00:0c:9f:f0:00 is the address of my computer.

Q7.
The hexadecimal value for the Frame Type is 0X0800. It cooresponds to the IP protocol.

Q8.
For some reason, the character 'O' did not print and I could not count the byte number. However, I have attached the screenshot for the captured packets listing to show where it lies.

Q9.
Multiple instances of the ARP table can be seen in the screenshot.
IP address is the IP protocol address, Physical address is the MAC address, HW type means the type of the hardware the network is using i.e., ethernet in our case, Iface is the interface that we are using on our machine for this communication.

Q10.
The source is 08:ed:b9:a1:76:95 and the destination is ff:ff:ff:ff:ff:ff.

Q11.
The hexadecimal value is 0X0806 and it refers to Address Resolution Protocol.

Q12.
a.At the byte after the first 20 bytes i.e., the 21st byte
b.0X0001
c.Yes
d.In the target MAC address, 00:00:00:00:00:00.

Q13.
a.After the first 20 bytes.
b.The value is 0X0002 for reply
c.In the sender's MAC address

15. It is because the ARP reply is sent back to the actual sender of the request.